## Slide 1: The National FAA Safety Team Presents
Airplane Weight and Balance
FAA Safety Seminar Attendees
W. J. Doyle, Jr., CFI A&I, AGI, IGI, FAAST Rep
05/21/2021 – 12/31/2021
Notes: (QMS File Number) Original Author: (Name) (MM/DD/YYYY); POC (Name), AFS-850 (Position), Office (NNN-NNN-NNNN); revised by (Name) (MM/DD/YYYY)
This is the title slide for (Insert Title Here)
Script - We have included a script of suggested dialog with most slides. The script will always appear in a non-italic font. Presenters may read the script or modify it to suit their own presentation style. See template slides 5 and 6 for examples of a slides with script.
Presentation Instructions - (stage direction and presentation suggestions) will be preceded by a Bold header: the instructions themselves will be in Italic fonts. See slides 2, 3, and 4 for examples of slides with Presentation Instructions only.
Program control instructions - will be in bold fonts and look like this: (Click) for building information within a slide; or this: (Next Slide) for slide advance.
Background information - Some slides may contain background information that supports the concepts presented in the program. Background information will always appear last and will be preceded by a bold Background: identification.
The production team hope you and your audience will enjoy the show. Break a leg!
(Next Slide)

## Slide 2: Welcome
Exits
Restrooms
Emergency Evacuation
Breaks
Sponsor Acknowledgment
Other information
Notes: Presentation Instruction: Here’s where you can discuss venue logistics, acknowledge sponsors, and deliver other information you want your audience to know in the beginning. You can add slides after this one to fit your situation.
(Next Slide)

## Slide 3: Airplane Weight and Balance
The Inherent Dangers of Weight and Balance Procedural Complacency
–
What You Don’t Know Can Get You and Your Passengers Killed!
Notes: Presentation Instruction: If you’ll be discussing additional items, add them to this list
(Next Slide)

## Slide 4: How to Download this Presentation
You can download this presentation at the link below.
  https://williamjdoylejr.net/FAAST/W&B/Weight_and_Balance_2021.pptx
  The link is case-sensitive
  If prompted for a password, click the “Read Only” button
  You can email me doylewj@ix.Netcom.com to request the link
Notes: Presentation Instruction: If you’ll be discussing additional items, add them to this list
(Next Slide)

## Slide 5: Presentation Agenda
Weight & Balance Accident Trends
Weight & Balance Accident Scenarios
Applicable FARs
Weight & Balance Concepts
Weight & Balance Terms
Weight & Balance Computations
Calculating Weight & Balance Using iPad and ForeFlight
Weight Impact on V-Speeds
How to Query the NTSB Database from a Web Browser
How to Query the NTSB Database from AOPA
Appendix: Weight & CG Change Formulas
Notes: Presentation Instruction: If you’ll be discussing additional items, add them to this list
(Next Slide)

## Slide 6: NTSB Statistics on Weight & Balance Accidents in the United States from 2000 to 2019

## Slide 7: NTSB Weight & Balance Accident Trends U.S. 2000 – 2019
70% of these accidents involved fatalities.
Notes: These statistics were drawn from the NTSB accident database at https://www.ntsb.gov/_layouts/ntsb.aviation/index.aspx
The search criteria were:
Date Range 01/01/2000 to 12/31/2019
Country – United States
Injury Severity: All
Category: Airplane
Operation: Part91:General Aviation
Key Words: “Weight and Balance“ or "weight and balance" or “Weight & Balance“ or "weight & balance"
The search returned 796 results that contained the above key words
The results were downloaded as an XML file
  The remaining statistics were done in Excel

## Slide 8: NTSB Weight & Balance Accident Trends U.S. 2000 – 2019
Notes: These statistics were drawn from the NTSB accident database at https://www.ntsb.gov/_layouts/ntsb.aviation/index.aspx
The search criteria were:
Date Range 01/01/2000 to 12/31/2020
Country – United States
Injury Severity: All
Category: Airplane
Operation: Part91:General Aviation
Key Words: “Weight and Balance“ or "weight and balance" or “Weight & Balance“ or "weight & balance"
The search returned 796 results that contained the above key words
The results were downloaded as an XML file
  The remaining statistics were done in Excel

## Slide 9: NTSB Weight & Balance Accident Trends U.S. – 2000 – 2019
TOW = Take-Off Weight
Many of these accidents had an AFT CG that was AFT of the CG limit
N4955A – 5 people (3 children ages 11, 12, 13)
N59532 – boy (age 4) not belted in, died of head trauma
N9456P – 6 people (all adults)

## Slide 10: NTSB Report ANC11FA037 on Cessna 180 N4955A Accident

## Slide 11: Cessna 180 N4955A – NTSB Report ANC11FA037
The accident occurred 5/27/2011
  Pilot had not flown since 6/12/2010 (lapse of 349 days)
  Pilot did not meet the FAA’s recent experience requirement for the required number of takeoff and landings to carry passengers.
    FAR 61.57: 3 takeoffs and landings within 90 days
  Pilot’s logbook noted about 4 hours in the accident airplane
Airplane’s estimated gross weight at the time of the accident was about 243 pounds over its approved maximum takeoff weight.
Witness accounts reported
  Airplane swerving off the runway during the takeoff roll
  Nose-high attitude and rapid roll prior to impact
Per NTSB, pilot likely lost control during the takeoff roll
  Pilot applied excessive nose-up pitch to become airborne.
  Once airborne, pilot failed to attain sufficient airspeed to avoid an aerodynamic stall
  Airplane descended out of control to the ground.

## Slide 12: Cessna 180 N4955A – NTSB Report ANC11FA037
Estimated Weight and Balance
  Due to the extensive fire damage, an exact weight and balance calculation could not be made.
  Pilot’s weight was taken from his most current FAA medical examination.
  Weight of the front seat passenger was taken from her reported weight on her Alaska driver’s license.
  Weights for the rear seat passengers (girls: ages 11 and 13, and boy: age 12) were estimated using the Centers for Disease Control (CDC) growth charts showing average weight by age and gender.

## Slide 13: Cessna 180 N4955A – NTSB Report ANC11FA037
Items of cargo that were identifiable are listed as follows:
  Chainsaw
  Pistol
  Multiple bags of food and grocery items
  Personal clothing and bags
  Pots
  Kitchen utensils
  Rope
  Bundle of electrical wire
Pilot’s son said that the airplane’s fuel tanks were completely filled prior to the accident flight from the pilot’s personal fuel storage tank.

## Slide 14: Cessna 180 N4955A – NTSB Report ANC11FA037
Estimated weights
  Basic Empty Weight (from March 5, 1991) – 1631 pounds
  Pilot and Front seat Passenger – 417 pounds
  Rear Seat Passengers – 293 pounds
  Cargo – 100 pounds
  Fuel (55 gallons) – 330 pounds
  Oil (12 quarts) – 22 pounds
The gross weight of the airplane at the time of the accident was estimated to be 2,793 pounds, or 243 pounds over the approved maximum takeoff gross weight for the airplane.
The estimated center of gravity at the time of the accident was positive 42.18 inches.
The center of gravity range at 2,550 pounds (maximum gross weight) is positive 39.5 inches to positive 45.8 inches

## Slide 15: NTSB Report WPR18FA119 on Piper PA24 N9456P 4/9/2018 Accident

## Slide 16: Piper PA24 N9456P – NTSB Report WPR18FA119
Pilot data
  Pilot’s first flight in accident airplane was 4/9/2018 from North Las Vegas Airport (VGT), NV to Scottsdale Airport (SDL), AZ.
  Pilot’s certificates
    ATP ASEL and AMEL
    CFI ASE, AME, IA
    Medical Certificate – 1st Class with the following limitation: "Not valid for any class after 08/31/2018."
  Pilot flight time
    Total flight time 5,200 hours
    Flight time in accident airplane was approximately 2 hours
Student Pilot data
  Student Pilot Certificate - none
  Medical Certificate - none
  Total Flight Time – could not be determined

## Slide 17: Piper PA24 N9456P – NTSB Report WPR18FA119
Toxicology Report
  Pilot Toxicology
    Negative for carbon monoxide, ethanol and all drugs tested
  Student Pilot Toxicology
    Negative for carbon monoxide and ethanol
    Testing identified benzoylecgonine in his blood and urine specimens and MDMA in his urine samples.
      Benzoylecgonine is an inactive metabolite of cocaine.
      MDMA is a controlled substance (Ecstasy)

## Slide 18: Piper PA24 N9456P – NTSB Report WPR18FA119
Airplane Data
  Make/Model – Piper PA24-260 (Comanche)
  Year of Manufacture – 1970
  Date/Type of Last Inspection – 12/01/2017, Annual
  Airframe Total Time – 6,158 Hours as of last inspection
  Certified Max Gross Weight – 3,200 lbs
  POH Aft CG – 93.0 inches
Accident Data
  NTSB determined takeoff weight – 3,335 lbs (135 lbs over gross)
  NTSB determined Aft CG – 95.2 inches (2.2 inches beyond Aft CG).
  NTSB also identified degraded engine power output due to a preexisting engine cylinder intake valve spring failure.

## Slide 19: Piper PA24 N9456P – NTSB Report WPR18FA119
The accident occurred 4/9/2018
  The airline transport pilot, student pilot, and four passengers departed on a cross-country flight from Scottsdale Airport (SDL), AZ to North Las Vegas Airport (VGT), NV.
  Seating
    The airline transport pilot occupied the right front seat
    The student pilot occupied the left front seat
    The four passengers occupied the two middle row and two aft row seats.
    Even though the student pilot was seated in the left seat, the investigation could not determine who was manipulating the flight controls when the accident occurred.

## Slide 20: Piper PA24 N9456P – NTSB Report WPR18FA119
Witnesses and airport surveillance camera video indicated that the airplane's wings were rocking during the departure and shortly after rotation.
The controller asked if the airplane was experiencing any difficulties; according to the controller, the pilot responded, “We're good. We're just in training mode."
One witness reported that the engine sounded as if it was not developing enough power.
The last recorded radar data point indicated that the airplane's altitude was about 200 ft above ground level.
A traffic camera, located about 0.5-mile northwest of the end of the runway, showed the airplane in a left bank turning left.
As the turn progressed, the bank angle increased, and the airplane started to descend.
The airplane's wings were nearly vertical before the airplane impacted terrain.
A post-crash fire ensued.

## Slide 21: Piper PA24 N9456P – NTSB Report WPR18FA119
Flight Events per NTSB
  Prior to flight - Aircraft loading event
  Initial climb - Loss of engine power (partial)
  Initial climb - Loss of control in flight
  Uncontrolled descent - Collision with terrain/object (non-CFIT)
Probable Cause per NTSB
  The National Transportation Safety Board determines the probable cause(s) of this accident to be:
    The flight instructor's failure to maintain airplane control during the initial climb as a result of the airplane being loaded above its maximum gross weight and beyond its aft center of gravity limits.
    Contributing to the accident was a degraded engine power output due to a preexisting engine cylinder intake valve spring failure, which further reduced the airplane's climb capability.

## Slide 22: Piper PA24 N9456P – NTSB Report WPR18FA119
NTSB Findings
  Aircraft-Aircraft oper/perf/capability-Aircraft capability-CG/weight distribution-Capability exceeded - Cause
  Aircraft-Aircraft oper/perf/capability-Aircraft capability-Maximum weight-Capability exceeded - Cause
  Aircraft-Aircraft power plant-Engine (reciprocating)-Recip eng cyl section-Fatigue/wear/corrosion - Factor
  Personnel issues-Task performance-Use of equip/info-Aircraft control - Pilot - Cause
  Personnel issues-Task performance-Planning/preparation-Weight/Balance calculations - Pilot

## Slide 23: Piper PA24 N9456P – NTSB Report WPR18FA119
Lessons learned and “take-aways”:
  Determine weight of each crew member and passenger and their baggage before each flight
    Verify using FBO’s scale or portable digital bathroom scale
  Calculate weight and balance before each flight
    Use a computational device such as a tablet, e.g. iPad
    Use an aviation application such as ForeFlight
    Refer to the POH often
  Make sure you are familiar with the airplane and proficient in flying it
    Schedule an orientation flight with a CFI who is proficient in the airplane, even if you are a CFI yourself
  For CFI’s
    Make sure you know something about your student before getting into an airplane with them

## Slide 24: Piper PA24 N9456P – NTSB Report WPR18FA119
NTSB Reports
  Aviation Accident Data Summary
    http://williamjdoylejr.net/FAAST/W&B/Accident_WPR18FA119_NTSB_Data_Summary.pdf
  Aviation Accident Final Report
    http://williamjdoylejr.net/FAAST/W&B/Accident_WPR18FA119_NTSB_Final_Report.pdf

## Slide 25: Are There Any FARs That Cover Weight & Balance?
Notes: FAR 91.103 – Preflight Action

## Slide 26: 14 CFR 91.103 – Preflight Action
Each pilot in command shall, before beginning a flight, become familiar with all available information concerning that flight. This information must include {but is not limited to} —
  For a flight under IFR or a flight not in the vicinity of an airport, weather reports and forecasts, fuel requirements, alternatives available if the planned flight cannot be completed, and any known traffic delays of which the pilot in command has been advised by ATC;
  For any flight, runway lengths at airports of intended use, and the following takeoff and landing distance information:
    For civil aircraft for which an approved Airplane or Rotorcraft Flight Manual containing takeoff and landing distance data is required, the takeoff and landing distance data contained therein; and
    For civil aircraft other than those specified in paragraph (b)(1) of this section, other reliable information appropriate to the aircraft, relating to aircraft performance under expected values of airport elevation and runway slope, aircraft gross weight, and wind and temperature.

## Slide 27: Weight & Balance Concepts from an Elementary School and Middle School Perspective

## Slide 28: How Much Can an Airplane Weigh?
Each airplane has a limitation called the maximum gross takeoff weight. Some airplanes also have a maximum gross landing weight.
This weight includes everything
    Airplane (empty)
    Fuel
    Pilot and passengers
    Baggage
There is another component called “Balance.”
The entire process is called “Weight and Balance.”

## Slide 29: What Does Balance Mean?
Classic example is the playground seesaw:
    Center bar is the fulcrum which is the center of gravity.
    Heavier weight of “big” kid on one end overcomes lesser weight of “little” kid on other end
    This forces the “little” kid to go up
    Is there a way to make the “big” kid go up without adding weight or changing kids?

## Slide 30: Weight & Balance Terms That All Pilots Should Know

## Slide 31: Weight & Balance Terms
Arm (moment arm)
  horizontal distance in inches from the reference datum line to the CG of an item.
  Arms ahead (forward) of the reference datum are minus (–)
  Arms behind (aft) of the reference datum are positive (+)
  When the reference datum is ahead of the airplane, all of the arms are positive and computational errors are minimized
Reference Datum
  imaginary vertical plane from which all distances are measured
Moment
      product of the weight of an item multiplied by its arm. Moments are expressed in inch-pounds (in-lb). Total moment = airplane weight * the distance between the datum and the CG.
Moment Index
  moment divided by a constant such as 100, 1,000, or 10,000. The purpose of using a moment index is to simplify weight and balance computations of aircraft where heavy items and long arms result in large, unmanageable numbers.

## Slide 32: Weight & Balance Terms
Station
      a location in the aircraft that is identified by a number designating its distance in inches from the datum. The datum is, therefore, identified as station zero. An item located at station +50 would have an arm of 50 inches.
Center of Gravity (CG)
      imaginary point when aircraft would balance if suspended, i.e. where all of its weight is concentrated
CG Limits
      forward and aft center of gravity locations within which the aircraft must be operated at a given weight

## Slide 33: Weight & Balance Terms
Usable Fuel
  fuel available for flight planning and during flight
Unusable Fuel
  fuel remaining in the airplane’s system after a run-out test
Basic Empty Weight
  weight of the standard airplane, optional equipment, unusable fuel, and full operating fluids, e.g. full engine oil
Total Weight (Gross Weight)
  total weight of airplane and everything it is carrying
  Takeoff & Landing weight limitations may be different (Note: Cessna 182 and Cirrus SR20)
Maximum Ramp Weight
  maximum weight limit for ground operations such as taxiing
Maximum Takeoff Weight
  maximum weight limit for taking off; may be more than landing weight
Maximum Landing Weight
  maximum weight limit for landing; may be less than takeoff weight

## Slide 34: Weight & Balance Terms
Maximum Weight
  weight limit set by the manufacturer
Maximum Zero Fuel Weight
  maximum weight exclusive of usable fuel
Useful Load
  maximum weight minus empty weight: weight available for crew, passengers, baggage, fuel
Payload – Important in CAP Context for C172/C182/U206 Missions
  useful load minus full fuel; weight available for air crew and baggage
Standard Weights
  fuel weighs 6 pounds per U.S. gallon
  oil weighs 7.5 pounds per U.S. gallon or 1.875 pounds per U.S. quart
Notes: Emphasize Payload importance

## Slide 35: Equipment List for Weight & Balance

## Slide 36: Weight & Balance Equipment List
The aircraft is furnished with an equipment list, which specifies
  all the required equipment
  all equipment approved for installation in the aircraft
The weight and arm of all installed equipment are included on the list and checked prior to the aircraft leaving the factory.
When an aircraft mechanic or repairman adds or removes any item on the equipment list,
  he or she must change the weight and balance record to indicate the new empty weight and EWCG
  the equipment list is revised to show which equipment is actually installed.
  FAA Aircraft Weight & Balance Handbook Figure 2-17 is a comprehensive equipment list that includes all of the items of equipment approved for this particular model of aircraft.

## Slide 37: Weight & Balance Equipment List
The pilot’s operating handbook (POH) for each individual aircraft includes an aircraft-specific equipment list of the items from this master list.
When any item is added to or removed from the aircraft, its weight and arm are determined in the equipment list and used to update the weight and balance record.
The POH and airplane flight manual (AFM) also contain CG moment envelopes and loading graphs. Examples of the use of these graphs are given in FAA Aircraft Weight & Balance Handbook Chapter 5, Single-Engine Aircraft Weight and Balance Computations.

## Slide 38: Weight & Balance Equipment List

## Slide 39: Weight & Balance Equipment List

## Slide 40: How to Calculate Weight & Balance

## Slide 41: Weight & Balance Computations Center of Gravity (CG)
CG Calculation – Computational Method
  By hand (may need for FAA knowledge test)
  Using an Excel spreadsheet
  Using ForeFlight on an iPad/iPhone
    or similar SmartPhone/tablet app
CG Calculation – Graphic Method

## Slide 42: Weight & Balance Computation Concepts
Calculating the Moment
  Given
    Arm = 100 inches
    Weight = 50 pounds
  Layout the formula
    Weight x Arm = Moment
    50 x 100 = 5,000
Notes: Moment = Weight x Arm

## Slide 43: Weight & Balance Computation Concepts
Illustration of Weight and Balance
Notes: How to figure the Arm necessary to balance a weight

## Slide 44: Weight & Balance Computation Concepts
Calculating the Balance
  Given
    Arm = 50 inches
    Weight = 50 pounds
    Arm = 25 inches
    Weight = 100 pounds
  Layout the formula
    Weight x Arm = Moment
    50 x 50 = 2,500
    100 x 25 = 2,500
    Total = 5,000
  Arm to balance a 50 lb weight
    Weight x Arm = Moment
    50 x ? = 5,000
    Moment ÷ Weight = Arm
    5,000 ÷ 50 = 100
Playground Seesaw Example
Moving the little kid to balance the big kid
Notes: How to figure the Arm necessary to balance a weight

## Slide 45: Weight & Balance Computation Concepts
Computational Method
  Aircraft Allowances:
    Maximum gross weight = 3,400 pounds
    CG range = 78–86 inches
  Given:
    Weight of front seat occupants = 340 pounds
    Weight of rear seat occupants = 350 pounds
    Fuel = 75 gallons
    Weight of baggage in area 1 = 80 pounds
  Problem to solve
    Is CG within range?
    Is weight <= gross weight?
Notes: CG = Total Moment / Total Weight

## Slide 46: Weight & Balance Calculation – Graph Method
Calculating an airplane’s CG via Graph Method
  To simplify calculations, the moment may sometimes be divided by 100, 1,000, or 10,000.
  Aircraft Allowances:
    Maximum gross weight = 2,400 pounds
  Given:
    Weight of front seat occupants = 340 pounds
    Weight of rear seat occupants = 300 pounds
    Fuel = 40 gallons
    Weight of baggage in area 1 = 20 pounds
  Problem to solve
    Is the Moment within range?
    Is weight <= gross weight?
CG = Moment x 1000 / Weight = ?
CG = 105.2 x 1000 / 2367 = 44.44

## Slide 47: Weight & Balance Calculation – Graph Method
Find weight for pilot and front seat passenger
Read from weight scale to diagonal line then straight down for moment
Record moment on worksheet
Repeat for rear seat passengers, baggage, and fuel
Find total weight and total moment lines on CG envelope graph
Check intersection of lines to see if within envelope
Notes: Steps for the Graph Method

## Slide 48: Weight & Balance Calculation – Graph Method

## Slide 49: Weight & Balance Calculation – Graph Method

## Slide 50: Weight & Balance Calculation – Graph Method

## Slide 51: Weight & Balance Calculation – Graph Method
Reference
  Pilots Handbook of Aeronautical Knowledge – Chapter 10
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/phak/media/12_phak_ch10.pdf
Cautions
  Slides 46, 47, and 48 should NOT be used for actual flight planning
  Refer to aircraft POH
    See next three slides for examples

## Slide 52: Weight & Balance Calculation – Graph Method for Cessna 182T NAV III

## Slide 53: Weight & Balance Calculation – Graph Method for Cessna 182T NAV III

## Slide 54: Weight & Balance Calculation – Graph Method for Cessna 182T NAV III

## Slide 55: Weight & Balance Computations
CG Computation -- Spreadsheet Method
Flight Scenario | Left Front | Right Front | Left Rear | Right Rear | Fuel in Gallons
#1 | Pilot: 280 lbs | Passenger: 200 lbs | N/A | N/A | 35
#2 | Pilot: 280 lbs | Passenger: 200 lbs | Cameras &Gear: 20 lbs | Passenger: 175 lbs | 53

## Slide 56: CG Calculation - Computational Method Excel Spreadsheet – Cessna 172S
Individual Items
  Item Name
  Item Weight
  Item Arm
  Item Moment (weight * arm)
CG inches
  Total Moment / Total Weight
CG Worksheet in Excel
  http://williamjdoylejr.net/FAAST/W&B/Weight_Balance_Cessna_172S.xls

## Slide 57: CG Calculation - Computational Method – Scenario #1

## Slide 58: CG Calculation - Computational Method – Scenario #1

## Slide 59: CG Calculation - Computational Method – Scenario #2

## Slide 60: Cessna 172S Center of Gravity Limits
Scenario #1 is within weight and CG limits
Scenario #2 exceeds weight and CG limits

## Slide 61: Cessna 172S CG-Moment Envelope
Scenario #1 is within weight and CG limits
Scenario #2 exceeds weight and CG limits

## Slide 62: Cessna 172S CG-Moment Envelope – Dangers and Limitations
Coffin Corner –
  Above gross weight limit
  Aft of Aft CG limit
  Stall-Spin accident in making
Normal Category – See POH
  No spins
Utility Category – See POH
  Spins may be okay

## Slide 63: Weight Impact on VSpeeds
Notes: As the airplane flies and burns fuel, the airplane gets lighter
As the airplane gets lighter, certain Vspeeds decrease

## Slide 64: Weight Impact on VSpeed
Excel Formula
=SQRT(Flying Weight Cell/Gross Weight Cell)*VSpeed Cell
Excel Examples
Notes: As the airplane flies and burns fuel, the airplane gets lighter
As the airplane gets lighter, certain Vspeeds decrease
Vspeeds in the POH are typically shown at gross weight

## Slide 65: Weight & Balance Scenarios
Notes: 65

## Slide 66: Weight & Balance Scenarios
Airplanes to be used for a cross country flight from Doylestown (KDYL) to Cape May (KWWD) and back
Crew weights and positions
Will each airplane be within weight and CG limits?

## Slide 67: Weight & Balance Scenario – C-172S – Full Fuel
Airplane 191 pounds overweight
CG above the envelope
Airplane not legal to fly
http://williamjdoylejr.net/FAAST/W&B/Weight_Balance_Cessna_172S.xls
Notes: Airplane is over gross and out of CG limit

## Slide 68: Weight & Balance Scenario – C-172S – Fuel to Tabs
Airplane 83 pounds overweight
CG above the envelope
Airplane not legal to fly
http://williamjdoylejr.net/FAAST/W&B/Weight_Balance_Cessna_172S.xls
Notes: The fuel could be reduced by 14 gallons to get within the weight limits, but that leaves only 21 gallons of fuel.
A flight from Doylestown Airport (KDYL) to Cape May County Airport (KWWD) would take approximately an hour and burn 9 to 10 gallons with only 11 or 12 gallons remaining.
FAR 91.151 - Fuel Requirements for Flight in VFR Conditions – 30 minute reserve for daytime flight
Return flight to KDYL not legal unless the airplane was refueled at KWWD

## Slide 69: Weight & Balance Scenario – C-182T – Full Fuel
Airplane 138 pounds overweight
CG above the envelope
Airplane not legal to fly
http://williamjdoylejr.net/FAAST/W&B/Weight_and_Balance_Cessna_182T.xls

## Slide 70: Weight & Balance Scenario – C-182T – Fuel to Tabs
Airplane within weight limit
CG within the envelope
Airplane is legal to fly
http://williamjdoylejr.net/FAAST/W&B/Weight_and_Balance_Cessna_182T.xls

## Slide 71: Weight & Balance Scenario – U-206H – Full Fuel
Airplane within weight and CG limits Airplane is legal to fly
http://williamjdoylejr.net/FAAST/W&B/Weight_Balance_Cessna_U206H.xls
Notes: With fuel to tabs, the airplane is within the weight and CG limits

## Slide 72: Weight & Balance Scenario – U-206H – Fuel to Tabs
Airplane within weight and CG limits Airplane is legal to fly
http://williamjdoylejr.net/FAAST/W&B/Weight_Balance_Cessna_U206H.xls
Notes: Airplane is within the weight and CG limits

## Slide 73: Weight & Balance Scenario – Cirrus SR20 – Full Fuel
Airplane 123 pounds overweight
CG above the envelope
Airplane not legal to fly
http://williamjdoylejr.net/FAAST/W&B/Weight_&_Balance_Cirrus_SR20.xls
Notes: Airplane is over gross and out of CG limit

## Slide 74: Weight & Balance Scenario – Cirrus SR20 –Tabs + 7
Airplane 27 pounds overweight
CG above the envelope
Airplane not legal to fly
http://williamjdoylejr.net/FAAST/W&B/Weight_&_Balance_Cirrus_SR20.xls
Notes: Airplane is over gross and out of CG limit

## Slide 75: Weight & Balance Scenario – Cirrus SR20 – Fuel to Tabs
Airplane within weight and CG limits
Airplane legal to fly
http://williamjdoylejr.net/FAAST/W&B/Weight_&_Balance_Cirrus_SR20.xls
Notes: A flight from Doylestown Airport (KDYL) to Cape May County Airport (KWWD) would take approximately an hour and burn about 12 gallons with only 14 gallons remaining.
FAR 91.151 - Fuel Requirements for Flight in VFR Conditions – 30 minute reserve for daytime flight
Return flight to KDYL not legal unless the airplane was refueled at KWWD

## Slide 76: Planning a Flight Calculating Weight & Balance Using ForeFlight Mobile Version 12.6 Apple iPad Air, iOS 12.4.8

## Slide 77: Planning the Flight – Weight & Balance
2005 Cessna 182T Weight Limitations – Is everything good to go?
  Gross Takeoff Weight = 3,100 pounds
  Basic Empty Weight = 2,060 pounds
  Maximum Useful Load = 1,040 pounds
  Crew, Fuel, and Flight Kits
    Pilot (left front) – 200 pounds
    Passenger (right front) – 245 pounds
    Pilot Flight Kit (left rear) – 10 pounds
    Passenger Flight Kit (right rear) – 10 pounds
    Baggage (chocks, tie-down ropes, oil, etc.) – 30 pounds
    Fuel (64 gallons - tabs) – 384 pounds

## Slide 78: Planning the Flight – Weight & Balance
See Pilot’s Guide to ForeFlight Mobile Version 13.3.2
  http://www.foreflight.com/ipad/guide/pdf
  Aircraft
    creating an aircraft: Pilot’s Guide pages 321-322
    deleting an aircraft: Pilot’s Guide page 325
  Weight & Balance: Pilot’s Guide page 320
See ForeFlight Mobile computation of weight & balance on following slides

## Slide 79: ForeFlight Mobile Weight & Balance
You can use these steps to start Weight & Balance calculation
  Launch ForeFlight Mobile
  See Menu Bar at bottom of ForeFlight display
  Tap the “More” button on Menu Bar to see menu
  Tap “Weight & Balance” in right pane of next slide
Tap “More” to See Menu

## Slide 80: ForeFlight Mobile Weight & Balance

## Slide 81: ForeFlight Mobile Weight & Balance

## Slide 82: ForeFlight Mobile Weight & Balance

## Slide 83: ForeFlight Mobile Weight & Balance – Setting Up An Airplane
This data is available from the weight & balance document in your airplane’s POH

## Slide 84: ForeFlight Mobile Weight & Balance – Setting Up An Airplane
This data is available from the weight & balance document in your airplane’s POH

## Slide 85: ForeFlight Mobile Weight & Balance – For A Given Flight
This data is unique to a given flight.
Crew weights, baggage weights, and fuel on board can vary.

## Slide 86: ForeFlight Mobile Weight & Balance – For A Given Flight
This data is unique to a given flight.
Crew weights, baggage weights, and fuel on board can vary.

## Slide 87: ForeFlight Mobile Weight & Balance – For A Given Flight
Compare this graph to the CG envelope in the Weight & Balance section of your airplane’s POH

## Slide 88: “After Class” Exercise
If you are a ForeFlight user, use ForeFlight Mobile to do a weight & balance computation:
  Setup your airplane
  Enter the following weights:
    Pilot & passenger
    Baggage
    Fuel in US gallons
  Determine the following:
    Is the airplane legal to fly based on its gross weight?
    Is the airplane legal to fly based on its CG envelope?
Feel free to use a different flight planning app as well as a different tablet or SmartPhone

## Slide 89: How to Query the NTSB Database
Notes: This section introduces the audience to NTSB accident database queries
89

## Slide 90: Accessing the NTSB Database
Use your web browser to access the NTSB Database
  http://www.ntsb.gov/_layouts/ntsb.aviation/index.aspx
Notes: If possible, demonstrate browser usage to the audience
If no Internet connection is available, walk the audience through these slides

## Slide 91: Accessing the NTSB Database
Notes: Here are step-by-step instructions on how to set up a query
Specify a date range.
You can optionally specify a City, if looking for a specific airport.
You can optionally specify a state. Click the drop-down button then type the first initial. “n” gets “Nebraska.” Pressing “n” three more times gets “New Jersey.”
The default for Injury Severity is “All.” You can also click on the drop-down button and select either “Non-Fatal” or “Fatal.”
Enter “United States” as the Country.
For Operation, recommend clicking the drop-down button and selecting “Part 91: General Aviation.”
You can optionally enter a keyword such as “crosswind.” Understand that this will get you every accident that has the keyword “crosswind” in it, which does not necessarily mean that it was a crosswind accident.
If you know the NTSB Accident Number, you can select a specific accident.

## Slide 92: Creating an NTSB Database Query
Notes: Here are step-by-step instructions on how to set up a query
You can optionally enter a keyword such as “Weight and Balance.” Understand that this will get you every accident that has the keyword Weight and Balance” in it, which does not necessarily mean that it was a weight and balance accident.
If you know the NTSB Accident Number, you can select a specific accident.
Click Submit Query when done

## Slide 93: Creating an NTSB Database Query

## Slide 94: Creating an NTSB Database Query

## Slide 95: How Many Weight & Balance Accidents in PA in Last 20 Years?
Notes: Usage of a keyword returns every accident report containing that key word. It does not necessarily mean that the key word caused the accident only that the key word is somewhere in the report.

## Slide 96
How Many Weight & Balance Accidents in PA in Last 20 Years?
Notes: Usage of a keyword returns every accident report containing that key word. It does not necessarily mean that the key word caused the accident only that the key word is somewhere in the report.

## Slide 97
How Many Weight & Balance Accidents in PA in Last 20 Years?
18 Accidents
Notes: Sample of what the query results look like

## Slide 98
How Many Weight & Balance Accidents in PA in Last 20 Years?
18 Accidents
Notes: Sample of what the query results look like

## Slide 99
How Many Weight & Balance Accidents in PA in Last 20 Years?
18 Accidents
56% had fatalities

## Slide 100
How Many Weight & Balance Accidents in NJ in Last 20 Years?

## Slide 101
How Many Weight & Balance Accidents in NJ in Last 20 Years?

## Slide 102
How Many Weight & Balance Accidents in NJ in Last 20 Years?
10 Accidents
Notes: Sample of what the query results look like

## Slide 103
How Many Weight & Balance Accidents in NJ in Last 20 Years?
10 Accidents
60% had fatalities

## Slide 104
How Many Weight & Balance Accidents in the Last 20 Years?
Spreadsheets built from the NTSB Database
    United States
      http://williamjdoylejr.net/FAAST/W&B/NTSB_Weight_and_Balance_2000-2019_3.xlsx
    Pennsylvania
      http://williamjdoylejr.net/FAAST/W&B/NTSB_Weight_and_Balance_2000-2019_PA.xlsx
      New Jersey
        http://williamjdoylejr.net/FAAST/W&B/NTSB_Weight_and_Balance_2000-2019_NJ.xlsx

## Slide 105: How to Use AOPA to Query the NTSB Database
Notes: This section introduces the audience to NTSB accident database queries Using AOPA
105

## Slide 106: Querying the NTSB Database from AOPA
Use your web browser to access AOPA
  https://www.aopa.org/
  Click TRAINING & SAFETY
  Click Air Safety Institute
Notes: If possible, demonstrate browser usage to the audience
If no Internet connection is available, walk the audience through these slides

## Slide 107: Querying the NTSB Database from AOPA
When you get to the Air Safety Institute
  Scroll down until you see Safety Content by Media Type

## Slide 108: Querying the NTSB Database from AOPA
When you get to the Air Safety Institute
  Scroll down until you see Safety Content by Media Type
  Click on Accident Analysis

## Slide 109: Querying the NTSB Database from AOPA
When you get to Accident Analysis
  Click on Accident Database
  You will then get a search form to complete

## Slide 110: Querying the NTSB Database from AOPA
When you get to Accident Analysis search form
  Complete the fields indicated below
  Scroll down to enter more search data

## Slide 111: Querying the NTSB Database from AOPA
As you continue the Accident Analysis search form
  Select PA 24 as the MODEL. This is a Piper Comanche.
  Select Fatal as the HIGHEST INJURY
  Click the SEARCH button

## Slide 112: Querying the NTSB Database from AOPA

## Slide 113: Querying the NTSB Database from AOPA
Clicking on the last accident on the page produces the following

## Slide 114: Parting Thoughts
Notes: Emphasize to the audience that they should seriously consider these items

## Slide 115: Weight & Balance Suggestions for Non-Owners
Set Yourself Up to Succeed
  Purchase the Airplane Information Manual for each non-owned airplane you fly
  Get a copy of the weight & balance sheet from the POH for each airplane you fly
  Get a weight & balance program and use it for each airplane you fly
    If a ForeFlight user, set up a ForeFlight weight & balance profile for each airplane you fly
    Build your own weight & balance spreadsheet for each airplane you fly
      If you are not computer savvy, find someone who is and ask them to help you build one
    Buy a weight & balance tablet app and use it for each airplane you fly
Find out the fuel policies for the non-owned planes you fly
  Civil Air Patrol
    Cessna 172 – full (40 gallons or 50 gallons depending on whether tanks are long range)
    Cessna 182 – tabs (64 gallons); NJWG uses 50 gallons
  Cirrus SR20 Flying Club
    Tabs + 7 (40 gallons)
  Cessna NAV III (G1000) Flying Club
    Cessna 172S – 35 gallons
    Cessna 182T – 64 gallons (tabs)
Notes: Think of this in terms of FAR 91.103
Getting the Airplane Information Manual is one of the best investments you can make

## Slide 116: Weight & Balance Pre-flight Planning
Do all weight & balance computations at home before you leave for the airport
  Get dressed weight from each passenger; explain to them the importance of accuracy
  Do a computerized calculation with your weight and your passenger(s) weights
  Figure out how much weight is available for fuel and luggage
  Tell your passenger(s) how much luggage they can bring
Don’t be afraid to “manage” your passenger(s)
  Explain to them how the regulations and safety apply to weight & balance
  Don’t be afraid to tell them that not everyone will “fit” onboard
  Don’t be afraid to tell them that certain luggage items will not “fit”
Do a thorough flight planning and fuel needs analysis
  Don’t cut the fuel too close – there could be unexpected complications
Notes: Think of this in terms of FAR 91.103
Do your planning at home, not on the fly at the airport
Explain the rules and expectations to your passengers beforehand

## Slide 117: The Three Most Useless Things to a Pilot
The runway behind you
  Moral: know your aircraft’s take-off minimums and calculate the weight and balance for your flight, your airport’s runway length, density altitude, any obstacles to be cleared
The altitude above you
  Moral: know your aircraft’s power settings for climb, cruise, and descent
The fuel on the ground below you
  Moral: know your aircraft’s fuel capacity, fuel system, GPH burn rate, and winds aloft for the route of flight.
Utilize superior judgment to avoid needing to use superior skill
Notes: Think of this in terms of FAR 91.103

## Slide 118
Notes: 118
Breath – enjoy!

## Slide 119: Credits and Information

## Slide 120: References and Information
Author of Presentation
  William J. Doyle, Jr., CFI A&I, AGI, IGI, Cessna CFAI
    FAA FAAST Team Representative, PHL FSDO
Downloading this presentation and associated spreadsheets
  https://williamjdoylejr.net/FAAST/W&B/Weight_and_Balance_2021.pptx
  http://williamjdoylejr.net/FAAST/W&B/Weight_Balance_Cessna_172S.xls
  http://williamjdoylejr.net/FAAST/W&B/Weight_and_Balance_Cessna_182T.xls
  http://williamjdoylejr.net/FAAST/W&B/Weight_Balance_Cessna_U206H.xls
  http://williamjdoylejr.net/FAAST/W&B/Weight_&_Balance_Cirrus_SR20.xls
Tom Woods (deceased), FAAST Rep PHL FSDO and NJWG/LGM
  for creating the W&B spreadsheets for Cessna 172S, 182T, and U206H
907 Flight Squadron and the Cirrus Owners and Pilots Association
  for sourcing the Cirrus SR20 W&B spreadsheet to me
Notes: How to download this presentation

## Slide 121: FAA Handbooks (1 of 2)
  Airplane Flying Handbook (FAA-H-8083-3B)
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/airplane_handbook/
Pilots Handbook of Aeronautical Knowledge (FAA-H-8083-25A)
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/phak/
  Risk Management Handbook (FAA-H-8083-2)
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/media/risk_management_hb_change_1.pdf
Advanced Avionics Handbook (FAA-H-8083-6)
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/advanced_avionics_handbook/
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/media/aah_errata.pdf
Notes: 121
Some good FAA References

## Slide 122: FAA Handbooks (2 of 2)
FAA Aircraft Weight & Balance Handbook – FAA-H-8083-1B
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/media/FAA-H-8083-1.pdf
Instrument Flying Handbook (FAA-H-8083-15B)
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/media/FAA-H-8083-15B.pdf
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/media/ifh_errata.pdf
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/media/ifh_addendum.pdf
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/media/ifh_addendum_b.pdf
  https://www.faa.gov/regulations_policies/handbooks_manuals/aviation/instrument_procedures_handbook/
Notes: 122
Some good FAA References

## Slide 123: References and Information
Dr. Al Schnur
  formula for recalculating Vspeeds for weights below gross weight.
  NTSB Accident Database
  http://www.ntsb.gov/_layouts/ntsb.aviation/index.aspx
Electronic Code of Federal Regulations – Title 14 Chapter I--Federal Aviation Administration, Department of Transportation
  Subchapter D – Airmen
  https://www.ecfr.gov/cgi-bin/text-idx?SID=d26e35f6991f05d99f5399e2671b5d3f&mc=true&tpl=/ecfrbrowse/Title14/14CIsubchapD.tpl
  Click on Part 61
  Subchapter F – Air Traffic and General Operating Rules
  Navigate to section using above link (Subchapter D – Airmen)
  Click on Part 91
Notes: 123
Some good FAA References

## Slide 124
Notes: 124
Breath – enjoy!

## Slide 125: Appendix Weight & CG Change Formulas
Notes: These formulas are from prior FAA Knowledge Tests

## Slide 126: Weight Change Formula
Changes in Weight and Moment

## Slide 127: Weight Change Formula
Airplane takes off with the following:
  Weight = 6,230 lbs
  CG = 79.0
What is the CG after 50 gallons of fuel burned from station 87?
Solution

## Slide 128: Weight Change Formula
Airplane takes off with the following:
  Weight = 3,000 lbs
  CG = 60.0
After takeoff
  25 gallons fuel burned at station 65
  200 lb passenger moves from station 50 to station 90
What is the resulting CG?
Solution

## Slide 129
Weight Shift Formula - CG Shifted by Weight Move
Airplane Gross Weight = 10,000 lbs; 500 lbs cargo shifts 50 inches.
How far does the CG move?

## Slide 130: Weight Shift Formula - Weight Shifted to Move CG Two Inches

## Slide 131
Weight Shift Formula - CG Shifted by Weight Move

## Slide 132: Weight Shift Formula - How Far to Move Weight to Shift CG

## Slide 133
This Completes
Airplane Weight & Balance The Inherent Dangers of Weight and Balance Procedural Complacency What You Don’t Know Can Get You and Your Passengers Killed!
FAA Customer Feedback Website
http://www.faa.gov/about/office_org/headquarters_offices/avs/offices/afs/qms/
PHL FSDO FAAST Program Manager – Eric Sieracki -
Eric.Sieracki@faa.gov
Notes: 133
Remind the attendees that they must sign in to be credited for attendance.
Ask for suggestions of any kind, especially what they would like to have presented as “elective” topics.

## Slide 134: Questions?
Notes: Presentation Instruction: You may wish to provide your contact information and main FSDO phone number here. Modify with
Your information or leave blank.
(Next Slide)

## Slide 135: Proficiency and Peace of Mind
Fly regularly with your CFI
Perfect Practice
Document in WINGS
Notes: There’s nothing like the feeling you get when you know you’re playing your A game and in order to do that you need a good coach (Click)
So fly regularly with a CFI who will challenge you to review what you know, explore new horizons, and to always do your best. Of course you’ll have to dedicate time and money to your proficiency program but it’s well worth it for the peace of mind that comes with confidence. (Click)
Vince Lombardi, the famous football coach said, “Practice does not make perfect. Only perfect practice makes perfect.” For pilots that means flying with precision. On course, on altitude, on speed all the time. (Click)
And be sure to document your achievement in the Wings Proficiency Program. It’s a great way to stay on top of your game and keep you flight review current.
(Next Slide)

## Slide 136: Thank you for attending
You are vital members of our GA safety community
Notes: Your presence here shows that you are vital members of our General Aviation Safety Community. The high standards you keep and the examples you set are a great credit to you and to GA.
Thank you for attending.
(Next Slide)

## Slide 137: Title
Sub Title
<Audience>
<Presenter>
< >
Notes: (The End)